## Slide 1
GUEST LECTURE · ELECTRONICS & INSTRUMENTATION ENGINEERING · VRSEC
AI and Digital Twins
in Instrumentation
What they actually do, what they aren't allowed to do, and where the trap is.
SHAFT f_r
29.95 Hz
OUTER RACE BPFO
107.4 Hz
VISIBLE IN A RAW FFT
NO
01 · KIRAN PRASAD GORLI · TORONTO
Notes: Do NOT introduce yourself yet. Ask the thermocouple question first: hands up if you had a lab where the reading drifted. Then, keep your hand up if the hard part was the physics of the sensor. Almost all hands drop. That is the talk.

## Slide 2
THE PREMISE
Instrumentation was never limited by our ability to measure.
It was limited by what we could do with the measurement.
That second half is the part that changed. That is where AI lives.
02 · OPEN
Notes: Deliver slowly. Everything in the lecture refers back to this line.

## Slide 3
CREDIBILITY, STATED UP FRONT
Who is talking, and how to discount him
WHAT I HAVE DONE
Graduate of this department
13 years consulting — TCS, Cognizant, Accenture
Enterprise document platforms for banks and insurers
Data pipelines and governance in a regulated industry
WHAT I HAVE NOT DONE
Never commissioned a control loop
Never signed off a safety instrumented system
Never worked a plant turnaround
If you work in automation, correct me in the Q&A
The model is never why these projects fail. The data pipeline, the failure modes and the trust are. Those lessons transfer completely.
03 · OPEN
Notes: Say the disclaimer plainly, do not soften it. Then pivot: your professors teach instrumentation better than you can; what nobody here can tell them is what the path from that chair to this one looks like.

## Slide 4
AGENDA
Five parts
1
The stack, honestly
8 min
Where AI sits, and where it is not allowed to sit
2
One failure, all the way down
18 min
A single bearing — geometry to signal processing to a decision
3
Demo one: Bearing Fault Lab
6 min
Take one measurement apart
4
Digital twins
11 min
The taxonomy, the trap, and demo two — held to its own test
5
What to learn, what the jobs are
6 min
Including which of your electives are worth picking
04 · AGENDA
Notes: Twenty seconds. They can read.

## Slide 5
CHECKED AGAINST VR20
Where this sits in your syllabus
YOU ALREADY HAVE THIS
Python — Semester II, core
FFT and filter design — DSP, Sem VI
Sampling and aliasing — DSP
PID and loops — Control Systems
PLC, DCS, SCADA — Industrial Automation
MPC — Computer Control of Processes
NOT IN YOUR SYLLABUS AT ALL
Hilbert transform and envelope detection
Probability and statistics — no course exists
Kurtosis and higher-order statistics
Vibration analysis and condition monitoring
Modbus, OPC UA, MQTT
Digital twins, anomaly detection
ELECTIVE ONLY — WHO TOOK IT?
IEC 61508 → Safety Instrumentation Systems
Historians, IIoT data flow → Industrial IoT
Machine learning → AI/ML in Healthcare
HART, PROFIBUS → Industrial Comm. Networks
Everything in the middle column is why this talk is worth an hour.
05 · YOUR CURRICULUM
Notes: Say plainly you read VR20 first — it buys credibility a CV cannot. Ask for a show of hands on the elective column. TIMING RISK: DSP is Semester VI; if this is a third-year room, add five minutes on the FFT.

## Slide 6
PART 1 · THE STACK
The chain has not changed
Process
Sensor
Signal
conditioning
ADC
Controller
Actuator
WHY 4-20 mA IS STILL 4-20 mA
Current, not voltage, because current does not care about lead resistance. Live zero at 4 mA so you can tell "reading zero" apart from "the wire is broken." That was good engineering in 1955 and it is good engineering now. HART still rides digital data on top of it. AI does not delete any of this — it sits on top of it.
06 · THE STACK
Notes: Be blunt that marketing implies the old stack is obsolete. It is not. It is the foundation.

## Slide 7
PART 1 · PURDUE MODEL
Where the layers sit
4 / 5
Enterprise IT
ERP, cloud, data lake
minutes to hours
3
Site operations
Historian, MES, batch records
seconds to minutes
2
Supervisory
SCADA, HMI — operators look here
sub-second
1
Basic control
PLC / DCS — PID on a deterministic scan
10–100 ms
0
The field
Sensors and actuators — physics
continuous
Going up trades latency for context — and data flows up far more freely than commands flow down. That asymmetry is a security control.
07 · THE STACK
Notes: VR20: Industrial Automation (core) already covers PLC/DCS/SCADA, so levels 1 and 2 are revision. Spend the time on level 3 and above, which is elective-only. The word Purdue appears nowhere in their syllabus.

## Slide 8
PART 1 · PROTOCOLS
How the data actually moves
4-20 mA / HART
Field device to controller. Analog loop with digital riding on top.
Modbus
Ancient, trivially simple, absolutely everywhere. No security whatsoever.
PROFINET / EtherNet/IP
Industrial fieldbuses on Ethernet.
OPC UA
The important one. Carries meaning, not just numbers — a tag knows it is a temperature in °C on a named asset.
MQTT + Sparkplug B
Lightweight publish/subscribe. How edge devices report upward.
Then it lands in a historian: AVEVA PI or AspenTech IP.21 in process industries; InfluxDB or TimescaleDB in newer stacks. If a vendor cannot tell you how their product gets data out of your DCS, they do not have a product — 90% of the work is here, at the boring integration layer.
08 · THE STACK
Notes: VR20: HART and PROFIBUS only appear in an ELECTIVE. Modbus, OPC UA and MQTT appear nowhere — zero hits for OPC. Ask who took Industrial Communication Networks; treat the last two as genuinely new.

## Slide 9
PART 1 · LATENCY BUDGET
The microsecond claim is wrong by 10,000×
Chart: milliseconds
| Hardwired trip | Edge inference | PLC scan cycle | Actuator response | Cloud round trip
Typical latency | 0.01 | 25 | 50 | 40 | 500
AI IN THE LOOP, REALISTIC
10–50 ms
HARDWIRED TRIP
<0.1 ms
Microsecond response belongs to hardwired interlocks and analog trip amplifiers. No software in the path — which is exactly why they are trusted with safety.
Cloud round trip is off the chart scale in practice — treat 500 ms as optimistic.
09 · THE STACK
Notes: Slow down. Imprecision on latency is how people get hurt.

## Slide 10
THE RULE
AI sits above the control layer,
not inside it.
It advises a human or a supervisory system. It rarely has direct authority over an actuator. It essentially never has authority over a safety function. We will come back to why.
10 · THE STACK
Notes: Let it sit for a beat. The SIL slide later pays this off.

## Slide 11
PART 2
One failure, all the way down
40–50%
of failures in electrical rotating machines are bearing failures
WHY THIS EXAMPLE, FOR EIGHTEEN MINUTES
It is not a toy — it is the single most common failure mode
The cleanest path I know from physics → signal processing → machine learning → a business decision
Everything is publicly verifiable: the bearing, the dataset, the arithmetic
And it shows exactly where the AI is, and how small that part is
11 · THE BEARING
Notes: Signal that this is the heart of the talk and you are slowing down.

## Slide 12
PART 2 · BEARING KINEMATICS
The physics gives you the answer first
THE CONSTRAINT
Balls roll rather than slide. That single constraint fixes the cage speed as a fraction of shaft speed. Everything else follows by counting how often a ball passes a defect.
n = ball count d = ball diameter
D = pitch diameter θ = contact angle
FTF
(f_r / 2) · (1 − (d/D)·cos θ)
cage rotation
BPFO
(n/2) · f_r · (1 − (d/D)·cos θ)
ball passes a fixed point on the outer race
BPFI
(n/2) · f_r · (1 + (d/D)·cos θ)
…on the rotating inner race
12 · THE BEARING
Notes: Derive out loud. The rolling constraint is the whole trick.

## Slide 13
PART 2 · WORKED NUMBERS
SKF 6205 at 1797 rpm
9 balls · d = 7.94 mm · D = 39.04 mm · θ = 0 · d/D = 0.2034
SHAFT f_r
29.95 Hz
CAGE FTF
11.93 Hz
OUTER BPFO
107.4 Hz
INNER BPFI
162.2 Hz
We know the frequency the fault will announce itself at — before measuring anything.
That is not machine learning. It is mechanics, and it is worth more than any model, because it turns an open-ended search into looking in one specific place.
One design detail worth noticing: BPFO is 3.585× shaft speed. Not 3, not 4. Manufacturers choose ball counts so defect frequencies are deliberately non-integer multiples — so faults cannot hide underneath shaft harmonics.
13 · THE BEARING
Notes: Do the arithmetic aloud. Pause after the boxed line — this is the point of the section.

## Slide 14
PART 2 · THE PROBLEM
So why can't we just take an FFT?
The fault is tiny
An early spall produces impacts of very low energy. In the demo, the 1× shaft line is about 170× larger than anything the defect puts at 107 Hz.
The fault is broadband
A very short impact is not narrowband. It does not deposit energy at 107 Hz — it rings the housing resonance, typically 2–15 kHz, which then decays.
The information is the rate
What carries the diagnosis is not the ringing frequency. It is how often the ringing repeats.
This is amplitude modulation: the defect modulates, the resonance carries. Demodulation is not in your syllabus — so we are going to build it from scratch, and it takes four minutes.
14 · THE BEARING
Notes: Do NOT say they already know AM — VR20 has no communications course and zero mentions of modulation. Set up the next slide instead.

## Slide 15
PART 2 · NOT IN YOUR SYLLABUS
Demodulation in four minutes
1
Take the DFT
The transform you compute with the FFT in DSP. For a real signal the spectrum is symmetric — the negative half mirrors the positive half and carries nothing new.
2
Delete the negative frequencies
Zero them. Double the positive ones so the energy still balances.
3
Transform back
What returns is complex-valued. This is the analytic signal, and the operation that produced it is the Hilbert transform.
4
Take the magnitude
Real squared plus imaginary squared, square rooted. The oscillation cancels and the outline survives. That outline is the envelope.
Why the magnitude kills the wiggle: if you have sin(t) and cos(t), the magnitude is exactly 1, forever. You have traded an oscillation for its amplitude.
15 · THE BEARING · scipy.signal.hilbert()
Notes: Do not rush. VR20 has no communications course, Signals and Systems was removed, DSP is 2 credits. This is new to everyone in the room. The sin/cos line is what makes it click.

## Slide 16
PART 2 · THE TECHNIQUE
Envelope analysis
1
Band-pass the resonance
2.4–4.0 kHz. Throwing away the low end deletes the shaft imbalance that was drowning everything.
2
Take the analytic signal
Hilbert transform, then magnitude. Carrier stripped, envelope left.
3
Remove DC, then FFT again
Transform the envelope itself, not the original signal.
4
Look at 107.4 Hz
A clean line at BPFO, with harmonics. Exactly where geometry said.
We used domain knowledge to build a feature in which the fault is obvious. Throw raw vibration at a deep network instead and you are asking it to rediscover the Hilbert transform and bearing kinematics from data. It might. It will need vastly more data, and you will not be able to explain what it learned.
16 · THE BEARING · KNOWN SINCE THE 1970s
Notes: Name it: envelope analysis / high-frequency resonance technique. Forty years older than the ML, and doing most of the work. Anchor step 1 to their DSP filter design — they have already designed this filter.

## Slide 17
PART 2 · THE MODEL
Now, finally, the machine learning
Notice how much smaller this section is than the signal processing. That ratio is correct.
FEATURES
RMS — total energy, rises late
Kurtosis — 4th moment, measures impulsiveness, rises early
Crest factor — peak / RMS
Envelope band energy at BPFO and harmonics
FRAMING A — SUPERVISED RUL
"This bearing has 340 hours left."
Needs run-to-failure data: machines deliberately instrumented and allowed to fail, repeatedly, across every mode you care about.
Ask how many companies have destroyed a statistically useful number of their own machines.
Essentially none. Which is why the same four public datasets appear in every paper.
FRAMING B — ANOMALY DETECTION
Train only on the healthy machine. Learn normal. Alarm on deviation.
Autoencoder reconstruction error, one-class SVM, isolation forest — or honestly, a control chart on kurtosis.
This is what actually gets deployed, because healthy data is the only thing you have a lot of.
17 · THE BEARING
Notes: Be explicit that Framing B is the real-world answer. Students always assume A. Ground kurtosis in the statistical treatment topic from Sensors and Transducers — VR20 has no statistics course.

## Slide 18
PART 2 · NOT IN THE TEXTBOOK
Why these projects fail
You have no labels
Not few. None. A thousand motors over five years might give you a dozen documented failures with usable data.
Models do not transfer
Different mounting stiffness moves the resonance. Domain shift is brutal. Note the physics transfers perfectly — BPFO is BPFO.
Sensor drift
Sensitivity shifts with temperature and age. A large share of anomaly alerts are instrumentation faults. Monitor your monitoring.
Alarm fatigue
The one that actually kills deployments. Next slide does the arithmetic.
Nobody set the threshold economically
It was set by optimizing F1 score instead of by costing out consequences.
The success stories are all in the vendor brochures. The failures are where the engineering is.
18 · THE BEARING
Notes: Spend real time here. This is what they will not get from a textbook or a vendor.

## Slide 19
PART 2 · ALARM FATIGUE
Do the arithmetic. Watch the number.
ASSETS MONITORED
500
FALSE POSITIVE RATE
1 %/day
FALSE ALARMS PER DAY
5
INVESTIGATION LOAD
15 hrs/day
THE BUDGET YOU ARE SPENDING
EEMUA 191 guidance: an operator can absorb roughly one alarm every ten minutes in steady state — across all alarm sources. Your analytics system competes for that budget with every process alarm in the plant.
WHAT ACTUALLY HAPPENS
By week three the engineers have learned the system cries wolf, and stop opening tickets. Six months later a real failure is flagged, ignored, and the machine fails.
The postmortem says the model was not accurate enough. The model was fine.
The threshold was set by a data scientist optimizing F1 instead of by an engineer costing out consequences.
19 · THE BEARING
Notes: Walk the numbers on the board. Make them watch 1% become 15 hours a day.

## Slide 20
PART 2 · THE RIGHT WAY
Set the threshold with a cost model
P* = C_FP / (C_FP + C_FN)
Alarm when the expected cost of not acting exceeds the cost of acting. C_FP is an unnecessary inspection; C_FN is an unplanned failure.
INSPECTION COST C_FP
$2k
UNPLANNED FAILURE C_FN
$200k
OPTIMAL THRESHOLD P*
1 %
So you should alarm at 1% confidence and accept many false positives — but only if you have the inspection capacity to absorb them. If you do not, the binding constraint is how many investigations your team can run per week. The threshold is a capacity planning decision, not a modelling decision.
20 · THE BEARING
Notes: Mention you have watched this exact argument in bank fraud detection. Same maths, same organizational failure.

## Slide 21
PART 2 · CONTROL
Where AI goes in control (mostly: not in the loop)
THE WORKHORSE — MPC
Model predictive control has been standard in refineries since the 1980s. It solves a constrained optimization at every step over a prediction horizon.
It handles what PID cannot: interacting variables, hard constraints, dead time. It is not machine learning — though its internal model can be learned.
REINFORCEMENT LEARNING — BE CAREFUL
RL learns by trying things. In a live process, "trying things" means potentially driving a reactor somewhere it should not go.
The well-known success is data centre cooling — and note how: advisory mode first, hard constraints, operator override at any time. A supervisory optimizer choosing setpoints, not a controller moving valves.
Honest state of the art: RL sets targets. Conventional control hits them.
21 · BEYOND THE BEARING
Notes: VR20 anchor: Computer Control of Processes (Sem VII, core) has a full unit on MPC — Dynamic Matrix Control included. Say 'MPC is coming in your Sem VII course; that is the thing that actually runs.'

## Slide 22
IF YOU REMEMBER ONE THING FROM THIS HOUR
You cannot assign a SIL rating
to a neural network.
IEC 61508 and 61511 govern safety functions. A Safety Integrity Level is a claim about probability of dangerous failure on demand — SIL 3 means between 1 in 1,000 and 1 in 10,000. To claim it you must demonstrate that rate with evidence, across the whole lifecycle.
You cannot enumerate its failure modes
You cannot bound behaviour on untested inputs
Its behaviour changes when you retrain it
Not AI pessimism. This is what mature safety engineering looks like — and the AI industry is slowly rediscovering it under the name "guardrails." You already have a discipline that solved this. Do not let anyone talk you out of it.
22 · IEC 61508 / 61511 · SECURITY EQUIVALENT: IEC 62443
Notes: Slow down completely. The SIS is separate, simple, deterministic, independently verified, and has final authority. If the AI is wrong, the SIS still trips. VR20 anchor: the Safety Instrumentation Systems elective (OE2, Sem VI) covers IEC 61508 and ISA SP84 — ask who took it before presenting this as new.

## Slide 23
PART 3 · DEMO ONE
Bearing Fault Lab
kiranic.com/lecture/bearing-lab.html
One measurement, taken apart. Raise the defect and watch where it shows up: barely in the raw spectrum, unmistakably in the envelope spectrum.
HEALTHY — BPFO INDEX
0.3
EARLY DEFECT — ALERT
3.1
ADVANCED — FAULT
7.6
SAME DEFECT, NOISY PLANT
1.6
Noisy plant — the false negative. Same 22% defect, nothing changed about the bearing — the index falls to 1.6 and the annunciator returns to NORMAL. The fault is missed, and nobody is told. A false alarm is annoying and visible; a missed detection is silent.
23 · DEMO ONE
Notes: THE MOMENT: on Early defect, ask the room to find the fault in the RAW spectrum and let them fail before you show the envelope — this was on the slide and is now yours alone, so do not forget it. Sequence: Healthy → Early defect (ask them to find it in the raw spectrum, let them fail) → drag RPM to show the peak tracking shaft speed → Advanced → Noisy plant. Alert threshold in the tool is 1.8, fault is 4.0. Noisy plant reads 1.3–1.9, so it creeps over the alert line only about one measurement in eight — that is the missed detection. Keep the local file open as a WiFi fallback.

## Slide 24
PART 4 · DIGITAL TWINS
What a digital twin actually is
A model of a physical asset, kept current by that asset's own data, that you can ask questions of. Not current → it is a simulation. Cannot be questioned → it is a dashboard.
1
Physics model
First principles — differential equations, FEA, kinematics. Accurate exactly where your equations are right. Slow, and it needs someone who understands the machine.
2
Data-driven surrogate
Trained to mimic the plant from its history. Fast. Interpolates well. Extrapolates terribly — hold that thought.
3
Hybrid
Physics model whose parameters are continuously re-estimated from live data. The interesting one, and by far the hardest to build.
You already built one this morning. When we derived BPFO from ball count and pitch diameter, we built a physics model of a bearing that predicts what the sensor will see. That is a twin component.
24 · DIGITAL TWINS
Notes: Two minutes. The term is abused harder than almost anything in industrial software, so be precise about the two conditions. The Part 2 callback matters — it tells the room they have already done level one without being told the name.

## Slide 25
PART 4 · WRITE THIS ONE DOWN
What does your twin predict
that a human could not —
and how was that validated?
No answer to the first half
It is a visualization.
No answer to the second half
It is a guess with good graphics.
A 3D model with live values painted on it fails both. It may be genuinely useful. It is not a twin — it cannot answer "what happens if I raise the feed rate ten percent."
25 · DIGITAL TWINS · THE VENDOR TEST
Notes: One minute. Tell them explicitly to write this down — it is the single most portable thing in the talk and it works on any vendor in any industry.

## Slide 26
PART 4 · THE INTELLECTUAL CORE
The trap: a fault is extrapolation
Five years of historian data
Almost entirely normal operation. A plant that failed often enough to give you a rich failure dataset would be a scrapyard.
The surrogate learns the healthy region
Inside it, the model interpolates — and interpolation is what these models are genuinely good at.
A fault is the machine leaving that region
By definition. A fault is the machine doing something it has not done before. That is what the word means.
So the model is excellent everywhere except the one place you bought it for.
And your validation set is also normal. Hold out 20% of five years of healthy data, test on it, R² comes back 0.99 — the metric that tells you it works is computed on the data that cannot tell you it works. That is structural. No architecture fixes it.
26 · DIGITAL TWINS · THE TRAP
Notes: Three minutes, and slow. Ask the room what is in five years of plant data and WAIT for an answer. The validation-set kicker is the part that surprises people — deliver it separately, after a pause. This is the thing that will still be true in ten years.

## Slide 27
PART 4 · DEMO TWO — A TWIN, HELD TO ITS OWN TEST
Live Condition Monitoring
kiranic.com/lecture/live-monitor.html
This is a level-one twin. There is no training data anywhere in it. It runs the bearing model from Part 2 forward in time — ball count and pitch diameter give BPFO, impacts ring the housing resonance, the spall grows — and computes what the accelerometer would see.
WHAT IT PREDICTS A HUMAN COULD NOT
Days-to-fault for MTR-402. A falsifiable claim about the future — you wait, and you see.
HOW WELL IT DOES
Confidently wrong early, swinging between numbers. It settles only once you could already read it off the chart.
Threshold 8: 0 false alarms, 22 d warning
Threshold 2: 4–5 per 30 d, 38–46 d warning
I left the projection crude deliberately. That is the honest state of most remaining-life numbers in the field — better you distrust them for the right reason than trust them for the wrong one.
27 · DIGITAL TWINS · DEMO TWO
Notes: Frame it AS A TWIN from the first sentence — this is the worked example for Part 4, not a second condition-monitoring demo. Open it before the lecture and leave it running from Part 1; it needs ~40 simulated days of trend. Then apply your own vendor test to it out loud, point at the projection box, and let it be wrong. Finish with the threshold slider: a prediction is only worth what you do with it.

## Slide 28
PART 4 · AND WHAT TO DO ABOUT IT
I hit this wall in my own house
THE WALL
A Raspberry Pi at home reads light, motion, temperature and proximity sensors and drives the automation. Sensors, controller, actuators — instrumentation at domestic scale.
I am exploring a data-driven surrogate on its history. Which means years of normal and not one failure.
THE HONEST RESPONSE
Stop trying to model the fault. Model NORMAL — learn what healthy looks like in detail, from the data you actually have, which is all healthy.
Then measure distance from it, and alarm on the distance.
You do not need to have seen a failure to know that today does not look like any day you have seen before.
That is Framing B from Part 2, and this is why it wins: it matches the data that exists rather than the data you wish you had. A twin that says "this is not normal, and here is which sensor is furthest out" is worth more than one claiming to predict a failure mode it has never observed.
28 · DIGITAL TWINS · THE RESPONSE
Notes: Two minutes, delivered as yourself. This is the most credible half-minute in the talk because it is the only place you have done the thing rather than described it. Do NOT end on the problem — the turn to modelling normal is the point, and it closes the loop back to anomaly detection.

## Slide 29
PART 4 · PHOTOGRAPH THIS SLIDE
What to learn, in this order
1
Statistics
The biggest hole in your degree — no probability or statistics course exists in eight semesters. Everything about thresholds and error rates is statistics.
2
The scientific Python stack
You have Python from Semester II. You do not have numpy, scipy.signal, pandas or scikit-learn. A different skill.
3
Signal processing past DSP
Two credits is not enough, and Signals and Systems was removed. Hilbert and envelope detection are not in it.
4
One time-series database
InfluxDB or TimescaleDB. Downsampling policies and retention.
5
OPC UA
Zero mentions in your syllabus — I checked. Python asyncua library. A real differentiator.
6
Classical ML before deep learning
Isolation forest, one-class SVM, PCA, gradient boosting. Precision and recall well enough to defend a threshold.
This list is built against VR20. I left out everything you already get.
29 · WHAT TO DO
Notes: Tell them explicitly to photograph it. The statistics point matters most — say it slowly.

## Slide 30
PART 4 · WORTH MONEY TO YOU
Choose your electives deliberately
Safety Instrumentation Systems
Open Elective 2, Sem VI
IEC 61508 and the protection-layer model. The most employable elective in your list, and almost nobody picks it. Everything on my SIL slide is in this course.
Industrial Internet of Things
Program Elective 3, Sem VII
Historians, industrial protocols, the SCADA to ERP data flow. The layer above where your core courses stop.
Real World Instrumentation with Python
Program Elective 5, Sem VII
Instrument systems, simulators, data I/O. The bridge from Semester II Python to actual instrumentation work.
AI and Machine Learning in Healthcare
Open Elective 2, Sem VI
The only real ML in your syllabus. The healthcare framing is incidental; the methods transfer.
The first and last are both Open Elective 2, so you must choose. Take the safety one — safety is much harder to self-teach and much harder to fake in an interview.
30 · WHAT TO DO
Notes: Thirty seconds. Most students pick electives by timetable convenience — this is concrete advice they can act on at registration.

## Slide 31
PART 4 · FREE, AND BETTER THAN A CERTIFICATE
A project you can start this week
Download the Case Western Reserve bearing dataset — public, the standard benchmark, and the exact 6205 bearing from today.
1
Reproduce today's demo on real data
Compute the envelope spectrum. Confirm the peak lands at the BPFO you calculated from geometry. When it does, you have verified theory against measurement — which is the actual job.
2
Build a detector trained only on healthy files
Anomaly detection, not classification. You do not have the labels for classification and neither does industry.
3
Report your false positive rate honestly
And argue for a threshold using a cost model you state explicitly. Almost nobody does this part.
Do step three and you can have a conversation in an interview that most candidates with a master's degree cannot have.
31 · WHAT TO DO · ALSO: NASA IMS, FEMTO/PRONOSTIA, C-MAPSS
Notes: Mean the last line seriously and say so.

## Slide 32
PART 4 · THE HONEST PART
The scarce skill is not the model.
"AI engineer" is mostly not where these jobs are. They are: controls engineer who can code. Reliability engineer who understands statistics. Data engineer who understands process. Architect who can talk to both the plant and IT.
The scarce skill is the person who understands the physical process AND the software. You are two years from being that person, and most of you do not realize it is valuable.
THE MISTAKE I MADE
I waited too long to learn the new tooling. I assumed depth in the old thing was enough. It was not, and the people who moved earlier had a far easier transition than I did.
Get deep in something real — EIE is something real. Then learn the tools relentlessly, starting now, not in year five. Depth plus current tooling is a very strong position. Either one alone is not.
32 · CLOSE
Notes: Deliver this as yourself, not as a lecturer. It is the part they will remember.

## Slide 33
APPENDIX · PHOTOGRAPH THIS ONE TOO
Cheat sheet
QUANTITY | FORMULA | 6205 @ 1797 rpm
Shaft | f_r = rpm / 60 | 29.95 Hz
Cage | FTF = (f_r/2)(1 − (d/D)cos θ) | 11.93 Hz
Outer race | BPFO = (n/2)·f_r·(1 − (d/D)cos θ) | 107.4 Hz
Inner race | BPFI = (n/2)·f_r·(1 + (d/D)cos θ) | 162.2 Hz
Ball spin | BSF = (D/2d)·f_r·(1 − ((d/D)cos θ)²) | 70.6 Hz
BSF note: a ball spall strikes both races once per ball revolution, so the observed line is usually 2 × BSF = 141.2 Hz. Published tables (including Case Western) tabulate that doubled value. Check the convention before hunting for a peak.
ENVELOPE SIGNATURES
Outer race — clean BPFO + harmonics, no sidebands. Easiest.
Inner race — BPFI with ±f_r sidebands.
Rolling element — BSF with cage-rate sidebands.
NUMBERS WORTH KEEPING
AI in loop: tens of ms, not µs
Bearing resonance: 2–15 kHz
Resolution = 1 / record length
P* ≈ C_FP / (C_FP + C_FN)
Standards: IEC 61508 / 61511 (SIL) · IEC 62443 (OT security) · ISO 20816 (vibration severity) · EEMUA 191 (alarms) · OPC UA = IEC 62541 · Purdue / ISA-95
33 · APPENDIX
Notes: Leave this up during Q&A.

## Slide 34
Questions.
Including the hostile ones.
Both simulators are yours. Open them, break them, read the source — every number in this talk was computed by that code, and it is about four hundred lines.
kiranic.com/lecture
Scan for both demos
34 · THANK YOU · KIRANIC.COM/LECTURE
Notes: If you do not know an answer, say so — in a room of engineers that raises your credibility rather than lowering it. Prepared answers are in the script: will AI replace instrumentation engineers; why not deep learning on raw signal; is the curriculum outdated; how much maths; LLMs in industry; and the 'you have never worked in a plant' question — take that one head on.